## Slide 1: FNAL results on tracking
Aiwu Zhang, Vallary Bhopatkar, Mike Phipps, Jessie Twigger, Marcus Hohlmann
HEP group A @ Florida Tech
2014-01-09

## Slide 2: Content
Focused on one data file:
-> this file has 100k raw events,;
-> the beam is 32GeV
-> test detectors are CMS with straight strips and two 10cm ZigZag detectors with 48 strips each
-> voltage on CMS is 3250V, while on 10cm ZZ detectors are 3900V
The tracking analysis is focused on the two 10cm ZZ detectors

## Slide 3: Cluster position distributions for reference detectors in X axis
1st tracker, 10cm
2nd tracker, 10cm
3rd tracker, 50cm
4th tracker, 10cm, FIT
A cut : number of strips in cluster >1 for all of the 4 detectors
-10
10
-10
10
0
20
-10
30
The red lines and numbers indicate the ranges that are selected for tracking. Will explain in later slides.

## Slide 4: Cluster position distributions for reference detectors in Y axis
1st tracker, 10cm
2nd tracker, 10cm
3rd tracker, 50cm
4th tracker, 10cm, FIT
A cut : number of strips in cluster >1 for all of the 4 detectors

## Slide 5: Cut conditions for tracking
Tested cut conditions:
Number of strips in cluster for reference detectors are larger than 1, i.e, at least 2 strips are fired in the event.
Cut X ranges on reference detectors to get more concentrated beam data (20mm in X aixs):
-10 to 10 for the 1st and 2nd ref. detectors
0 to 20 for the 3rd ref. detector, and
-10 to 30 for the 4th ref. detector.
(3) Cut on two 10cm ZZ detectors:
-> cluster position in ONE detector >= 0, either in upstream or downstream detector
-> number of strips in cluster for BOTH detectors > 0 and > 1
Cut conditions (1) and (2) are set as default,
and cut condition (3) gives FOUR groups of different cuts.
For each cut condition, the tracking is done with both exclusive fitting and inclusive fitting, and a geometric average of them is calculated.

## Slide 6: Residual distributions for the two 10cm ZZ detectors
Exclusive fitting
Exclusive fitting
Inclusive fitting
Inclusive fitting
Upstream detector
Downstream detector
Upstream detector
Downstream detector
Cut condition: (1) default cut on reference detectors;
(2) Position on upstream 10cm ZZ detector >=0 & number of strips >0
σ=0.4383
σ=0.4429
σ=0.3448
σ=0.3375

## Slide 7: Residual distributions for the two 10cm ZZ detectors
Exclusive fitting
Exclusive fitting
Inclusive fitting
Inclusive fitting
Upstream detector
Downstream detector
Upstream detector
Downstream detector
Cut condition: (1) default cut on reference detectors;
(2) Position on upstream 10cm ZZ detector >=0 & number of strips >1
σ=0.3956
σ=0.428
σ=0.3011
σ=0.3282

## Slide 8: Residual sigma table for the two 10cm ZZ detectors of the FOUR groups of cut conditions
 | Downstream detector |  |  | Upstream detector |  | 
Cut | Exclusive fitting | Inclusive fitting | Geometric average | Exclusive fitting | Inclusive fitting | Geometric average
Position in upstream detector >=0 & number of Strips in both > 0 | 0.4429 ±0.0119 | 0.3375 ±0.0090 | 0.3867 ±0.0147 | 0.4383 ±0.0118 | 0.3448 ±0.0077 | 0.3887 ±0.0136
Position in downstream detector >=0 & number of Strips in both > 0 | 0.4222 ±0.0108 | 0.3338 ±0.0078 | 0.3754 ±0.0130 | 0.4149 ±0.0096 | 0.325 ±0.0090 | 0.3672 ±0.0133
Position in upstream detector >=0 & number of Strips in both > 1 | 0.428 ±0.018 | 0.3282 ±0.0106 | 0.3748 ±0.0199 | 0.3956 ±0.0123 | 0.3011 ±0.0088 | 0.3451 ±0.0147
Position in downstream detector >=0 & number of Strips in both > 1 | 0.4062 ±0.0125 | 0.3077 ±0.0102 | 0.3535 ±0.0160 | 0.3889 ±0.0111 | 0.3004 ±0.0100 | 0.3418 ±0.0150
The default cut of X ranges for reference detectors are used for all of them.
Inclusive fitting yields a better resolution of ~ 300μm,
Geometric average is calculated as , geometric average resolution is ~350μm

## Slide 9: Residuals for reference detectors
REF2X
REF3X
UVA3X
REF1X
REF2Y
REF3Y
UVA3Y
REF1Y
σ=64.75μm
σ=89.02μm
σ=77.18μm
σ=85.57μm
σ=80.05μm
σ=59.16μm
σ=81.53μm
σ=88.75μm
Residual distributions for reference detectors show the tracking is working pretty good.

## Slide 10: Summary
Tracking is working nicely. Currently we are getting a resolution of 300~400μm for the 10cm ZZ detectors with 48 strips.
The strip pitch in this case is ~2mm (not a constant because of radial shape, note that angle between strips is 0.075 degrees), a simple calculation for reference.
Will need to apply a lot of cut conditions to see if the resolution could be improved.
The resolution may give information about how the charge sharing happens on the zigzag strips , which could bring us to a new/better design of the zigzag strips. So that better resolution could be reached.
Similar tracking studies will be made for other zigzag detectors and CMS detector with straight strips.